## Slide 1: Module 1 Basics of Statics
By
Dr. S.JEYANTHI,
SMEC,9840477440
Jeyanthi.subramanian@vit.ac.in
Cabin no-SOM LAB-AB1 006
BMEE201L Engineering Mechanics
School of Mechanical Engineering
Winter 21-22

## Slide 2: MODULE 1
Module:1 Statics of Particles
Fundamental concepts and principles - Resolution of a force -Resultant of forces in a plane-Equilibrium of a particle in a plane; Addition of concurrent forces in space- Equilibrium of a particle in space.

## Slide 3: Why engineering mechanics?
You have to design a car, which can run at a speed of 80 km/hr. In order to do this, you have to find engine power and the forces acting on the car body.
To design a dam structure, you need to compute of deflections and internal forces within structures

## Slide 4: What is engineering mechanics?
It is a branch of science which deals with the behavior of body at rest or in motion under the action of forces.
Mechanics
Mechanics of Fluids
Kinematics
Kinetics
Mechanics of
Deformable bodies
Mechanics of
Rigid bodies
Statics
Dynamics
Statics:
Bodies at rest (Equilibrium of bodies i.e. no motion) under action of Forces.
Dynamics: Motion of bodies
- without considering force
- considering force

## Slide 5: Outline
Forces in plane
  Resultant
    Two forces -parallelogram and triangular law
    Resultant of several forces - polygon law and rectangular components
  Equilibrium of a particle
    Free body diagram
    Lami’s theorem
    Rectangular components
Forces in space
  Rectangular components
  Resultant
  Equilibrium of a particle

## Slide 6
Particle
Rigid Body
Equilibrium
Newton’s Laws
Lami’s Theorem
Paralellogram Law
Principle of Transmissibility
Force
Moment
Couple
Resultant
Keywords

## Slide 7: What do they do?

## Slide 8: How do they feel ?

## Slide 9: Force
A physical quantity
brought into equilibrium
gravity

## Slide 10: Representation
Magnitude
Direction
Point of application
Line of action

## Slide 11
Particle: Body of negligible dimensions
Rigid body: Body with negligible deformations
Non-rigid body: Body which can deform
Particle? Rigid body? Deformable body?
In Statics, bodies are considered rigid unless stated otherwise.
Continuum: Body is assumed to consist of continuous distribution of matter

## Slide 12
Basic Concept - Definition
Space: Collection of points whose relative positions
can be described using “a coordinate system”
Time : For relative occurrence of events
Mass : - A measure of how much matter is in an object.
For example, a gold bar is quite small but has a mass of 1 kilogram, so it contains a lot of matter.
- It is a measure of the inertia of a body, which is its resistance to a change of velocity.
position,
velocity,
acceleration

## Slide 13
FPS – Foot pound second
CGS – Centimetre Gram Second
MKS – Metre Kilogram Second
SI – System International
Types of UNIT

## Slide 14
The SI unit of force magnitude is the newton (N) or kg·m/s2 or kg·m · s – 2
Resultant of a force system is a single force which produces the same effect as that of the force system. It is the equivalent force all the given forces.
Resolution of a force is the process of splitting up the given force into number of components.
Basic Concept - Force
Force : Vector quantity that describes an action of
one body on another.

## Slide 15
Force - Examples

## Slide 16
A group of forces acting together on a body
Classification:
Force System

## Slide 17: Classification
Collinear
Concurrent
Parallel
Non-concurrent non-parallel

## Slide 18: Collinear Forces

## Slide 19: Concurrent Forces
In Plane (2D)
In Space (3D)

## Slide 20: Parallel Forces
In Plane (2D)
In Space (3D)

## Slide 21: Non-parallel and non-concurrent

## Slide 22
Type of Force System

## Slide 23: Forces in Plane-Resultant
Parallelogram law
Triangular law
Polygon law
Rectangular components
P
Q
θ
α
R

## Slide 24
Resultant Force Finding Methods
Analytical Method
  Trignometric Method (Parallelogram formula, Lami’s theorem)
  Resolution Method
Graphical Method
  Triangle Law of Forces
  Polygon Law of Forces

## Slide 25
THE PARALLELOGRAM LAW

## Slide 26
Parallelogram Law - Problem

## Slide 27
Derived Laws
Triangle Law of Forces
If two forces acting on a body are represented by the sides of a triangle, their resultant is represented by the closing side of the triangle taken from first point to the last point.

## Slide 28
Derived Laws
Lami’s Theorem
If three forces acting at a point are in equilibrium, each force is proportional to the sine of the angle between the other two forces.

## Slide 29
Derived Laws
Polygon Law of Forces
If a number of concurrent forces acting simultaneously on a body are represented in magnitude and direction by the sides of a polygon, taken in order, then the resultant is represented in magnitude and direction by the closing side of the polygon.

## Slide 30
Derived Laws
Polygon Law of Forces
If a number of concurrent forces acting simultaneously on a body are represented in magnitude and direction by the sides of a polygon, taken in order, then the resultant is represented in magnitude and direction by the closing side of the polygon.

## Slide 31
Resolution of forces
Forces acting at some angle from the coordinate axes can be resolved into mutually perpendicular forces called components.
The component of a force parallel to the x-axis is called the x-component, parallel to y-axis the y-component, and so on.

## Slide 32
Resolution of forces
Components of a Force in XY Plane

## Slide 33
Resolution of forces
Components of a Force in 3D Space

## Slide 34
Resolution of forces
To find a resultant of number of forces,
  Determine horizontal and vertical components of all forces.
  Add horizontal forces (Fhoriz or Fx = F cos θ ).
  Similarly, add Vertical Forces (Fvert or Fy = F sin θ ).
  Find Magnitude and direction of the resultant force

## Slide 35
Resolution of forces – Single Force Example

## Slide 36: Rectangular Components of a Force

## Slide 37: Example 1
A force of 800 N is exerted on a bolt A as shown in Figure. Determine the horizontal and vertical components of the force.

## Slide 39
A man pulls with a force of 300 N on a rope attached to a building, as shown in Figure. What are the horizontal and vertical components of the force exerted by the rope at point A ?
Example 2

## Slide 41: Resultant of Several Concurrent Forces

## Slide 42: Class Problem 3

## Slide 43
First resolved all the forces in vertical and horizontal directions;
Let ∑H = Sum of Horizontal components
∑V = Sum of Vertical components
∑H = 150 cos 30° + 80 cos 110° + 110 cos 270° + 100 cos 345° = 199.13N..........(i)
∑V = 150 sin 30° + 80 sin 110° + 110 sin 270° + 100 sin 345° = 14.29N

## Slide 44
R = (∑H2 + ∑V2)1/2 = {(199.13)2 + (14.29)2}1/2
R = 199.6N
Let angle made by resultant is θ
tanθ = ∑V/∑H = 14.29/199.13 = 4.11º

## Slide 45: Class Problem 1
The two forces P and Q act on a bolt A. Determine their resultant.

## Slide 46: Solution
A parallelogram with sides equal to P and Q is drawn to scale.
The magnitude and direction of the resultant or of the diagonal to the parallelogram are measured,
A triangle is drawn with P and Q head-to-tail and to scale.
The magnitude and direction of the resultant or of the third side of the triangle are measured,
Graphical solution

## Slide 47
Apply the triangle rule, From the Law of Cosines,
From the Law of Sines,
Trigonometric solution

## Slide 48: Determine the resultant of the three forces of Problem

## Slide 51: Determine the x and y components and ,resultant

## Slide 54: Free Body Diagram
Free body diagram is a sketch of the isolated body, which shows the external forces on the body and the reactions exerted on it by the removed elements.
Procedure:
Isolate each body from the system
Indicate all the forces acting on it including the weight
Indicate all reactions
Show the dimensions and angles and reference axes

## Slide 55: Free Body Diagram-Cable and Spring

## Slide 56: Draw Free Body Diagram

## Slide 57: Equilibrium of a Particle
The particle is in equilibrium when R=ΣF=0
Lami’s Theorem:
If three concurrent forces are acting on a body, kept in an equilibrium, then each force is proportional to the sine of the angles between the other two forces and the constant of proportionality is the same.

## Slide 61
In a ship-unloading operation, a 3500 N automobile is supported by a cable. A rope is tied to the cable at A and pulled in order to centre the automobile over its intended position. The angle between the cable and the vertical is 2°, while the angle between the rope and the horizontal is 30°. What is the tension in the rope?
Class Problem 4

## Slide 62
Construct a free-body diagram for the particle at A.
Apply the conditions for equilibrium.
Solution

## Slide 63
Tutorial Problem 2
Determine the magnitude and direction of the smallest force F which will maintain the package shown in equilibrium. Note that the force exerted by the rollers on the package is perpendicular to the incline.
F = 76.1 N
α = 15°

## Slide 64
Solution
For minimum F, θ is 90°

## Slide 70
Tutorial Problem 3
A 160-kg load is supported by the rope-and-pulley arrangement shown. Knowing that β = 20°, determine the magnitude and direction of the force P that must be exerted on the free end of the rope to maintain equilibrium.
P = 602 N
α = 46.8°

## Slide 71
Tutorial Problem 4
Two forces P and Q are applied as shown to an aircraft connection. Knowing that the connection is in equilibrium and that P = 500 N and Q = 650 N, determine the magnitudes of the forces exerted on the rods A and B.

## Slide 72: Rectangular component of a Force in Space

## Slide 75: Force Defined by its Magnitude and Two Points on its Line of Action

## Slide 76: ADDITION OF CONCURRENT FORCES IN SPACE

## Slide 77
A tower guy wire is anchored by means of a bolt at A. The tension in the wire is 2500 N. Determine
the components Fx, Fy, Fz of the force acting on the bolt,
the angles θx, θy, θz defining the direction of the force.
Class Problem 4
Fx = -1060 N; Fy = 2120 N; Fz = 795 N

## Slide 81
Knowing that the tension in cable AB is 1425 N, determine the components of the force exerted on the plate at B.
Tutorial Problem 5
-1125 N, 750 N, 450 N

## Slide 83
Tutorial Problem 6
Find the magnitude and direction of the resultant of the two forces shown knowing that P = 300 N and Q = 400 N.

## Slide 85: Equilibrium of a Particle in Space
A 200-kg cylinder is hung by means of two cables AB and AC, which are attached to the top of a vertical wall. A horizontal force P perpendicular to the wall holds the cylinder in the position shown. Determine the magnitude of P and the tension in each cable.
Class Problem 5
P = 235 N
TAB = 1402 N
TAC = 1238 N

## Slide 86
Tutorial Problem 7
Three cables are used to tether a balloon as shown.
Determine the vertical force P exerted by the balloon at A knowing that the tension in cable AB is 259 N.
Determine the vertical force P exerted by the balloon at A knowing that the tension in cable AD is 481 N.
P = 1031 N
P = 926 N