## Slide 1: Introduction
In this presentation, the kinematics of rigid bodies will be considered
The relations existing between the time, the positions, the velocities, and the accelerations of the various particles forming a rigid body are investigated

## Slide 2
Types of Rigid-Body Motion
Translation
Rotation about a Fixed Axis
General Plane Motion
Motion about a Fixed Point
General Motion

## Slide 3
1. Translation
A motion is translation if any straight line inside the body keeps the same direction during the motion
All the particles forming the body move along parallel paths
If these paths are straight lines, the motion is said to be a rectilinear translation
If the paths are curved lines, the motion is a curvilinear translation
All the points of the body have the same velocity and the same acceleration at any given instant

## Slide 4
2. Rotation about a Fixed Axis
The particles forming the rigid body move in parallel planes along circles centered on the same fixed axis
If this axis, called the axis of rotation, intersects the rigid body, the particles located on the axis have zero velocity and zero acceleration

## Slide 5
Angular Displacement
in time is called as angular displacement
By convention anticlockwise displacement is positive
When the particle moves from A to B, other particles (say A1) on the same radial line also get displaced (from A1 to B1) through the same angle
The angular displacement of every particle in fixed rotation remains the same

## Slide 6
Angular Velocity
As we know that all the particles undergo same displacement in a given time interval, their angular velocity is also the same

## Slide 7
Angular Acceleration
Angular acceleration is also same for all the particles in the rigid body
In fixed axis rotation, the angular displacement, velocity and acceleration are same for every particle in the body
Hence, by describing the motion of one particle in the body, the motion of the entire body can be described
Unit for angular acceleration is rad/s2

## Slide 8
Equations Defining the Rotation of a Rigid Body about a Fixed Axis
Uniform Rotation
Uniformly Accelerated Rotation

## Slide 9
Relationship between Angular and Linear Motions
Tangential acceleration,
Normal acceleration,

## Slide 10: Problem 1
Cable C has a constant acceleration of 9 m/s2 and an initial velocity of 12 m/s, both directed to the right. Determine (a) the number of revolutions of the pulley in 2 s, (b) the velocity and change in position of the load B after 2 s, and (c) the acceleration of the point D on the rim of the inner pulley at t = 0.

## Slide 11
Solution
a. Motion of Pulley
The tangential velocity and acceleration of D are equal to the velocity and acceleration of C.

## Slide 12
Using the equations of uniformly accelerated motion, we obtain, for t = 2 s,

## Slide 13
b. Motion of Load B
Displacement of B in y-direction,

## Slide 14
c. Acceleration of Point D at t = 0

## Slide 15
A pulley and two loads are connected by inextensible cords as shown figure. The pulley starts from rest at t = 0 and is accelerated at the uniform rate of 2.5 rad/s2 clockwise. At t = 5 s, determine the velocity and position of load A and load B.
Problem 2

## Slide 16
3. General Plane Motion
Motions in which all the particles of the body move in parallel planes
Any plane motion which is neither a rotation nor a translation is referred to as a general plane motion

## Slide 17
4. Motion about a Fixed Point
The three-dimensional motion of a rigid body attached at a fixed point O, e.g., the motion of a top on a rough floor, is known as motion about a fixed point

## Slide 18
5. General Motion
Any motion of a rigid body which does not fall in any of the categories above is referred to as a general motion

## Slide 19
General Plane Motion
A plane motion which is neither a rotation nor a translation
However, a general plane motion can always be considered as the sum of a translation and a rotation

## Slide 21: Absolute and Relative Velocity in Plane Motion
Any plane motion can be replaced by a translation of an arbitrary reference point A and a simultaneous rotation about A.

## Slide 22
Assuming that the velocity vA of end A is known, wish to determine the velocity vB of end B and the angular velocity w in terms of vA, l, and q.
The direction of vB and vB/A are known. Complete the velocity diagram.

## Slide 23
Selecting point B as the reference point and solving for the velocity vA of end A and the angular velocity w leads to an equivalent velocity triangle.
vA/B has the same magnitude but opposite sense of vB/A. The sense of the relative velocity is dependent on the choice of reference point.
Angular velocity w of the rod in its rotation about B is the same as its rotation about A. Angular velocity is not dependent on the choice of reference point.

## Slide 24: Absolute and Relative Acceleration in Plane Motion
Relative acceleration associated with rotation about A includes tangential and normal components,
Absolute acceleration of a particle of the slab,

## Slide 25
Given determine
Vector result depends on sense of and the relative magnitudes of
Must also know angular velocity w.

## Slide 26: Absolute and Relative Acceleration in Plane Motion
x components:
y components:
Solve for aB and a.
Write in terms of the two component equations,

## Slide 27: Analysis of Plane Motion in Terms of a Parameter
In some cases, it is advantageous to determine the absolute velocity and acceleration of a mechanism directly.